## Slide 1
H-code (1) | Health Hazards Hazard statement (2) | Health Hazards Hazard classification(3)
H200 | Unstable explosive | Unstable explosive
H201 | Explosive; mass explosion hazard | Explosive division 1.1
H202 | Explosive; severe projection hazard | Explosive division 1.2
H203 | Explosive; fire, blast or projection hazard | Explosive division 1.3
H204 | Fire or projection hazard | Explosive division 1.4
H205 | May mass explode in fire | Explosive division 1.5
H220 | Extremely flammable gas | Flammable gas category 1
H221 | Flammable gas | Flammable gas category 2
H222 | Extremely flammable aerosol | Flammable aerosol category 1
H223 | Flammable aerosol | Flammable aerosol category 2
H224 | Extremely flammable liquid and vapour | Flammable liquid category 1
H225 | Highly flammable liquid and vapour | Flammable liquid category 2
H226 | Flammable liquid and vapour | Flammable liquid category 3
H227 | Flammable liquid | Flammable liquid category 4
H228 | Flammable solid | Flammable solid category 1 Flammable solid category 2
H240 | Heating may cause an explosion | Self-reactive chemicals type A Organic peroxides type A
H241 | Heating may cause a fire or explosion | Self-reactive chemicals type B Organic peroxides type B
H242 | Heating may cause a fire | Self-reactive chemicals type C and D Self-reactive chemicals type E and F Organic peroxides type C and D Organic peroxides type E and F
H250 | Catches fire spontaneously if exposed to air | Pyrophoric liquid category 1 Pyrophoric solid category 1
H251 | Self-heating; may catch fire | Self-heating chemicals category 1
H252 | Self-heating in large quantities; may catch fire | Self-heating chemicals category 2
H260 | In contact with water releases flammable gases which may ignite spontaneously | Chemicals which, in contact with water, emit flammable gas category 1
H261 | In contact with water releases flammable gases | Chemicals which, in contact with water, emit flammable gas category 2 and 3
H270 | May cause or intensify fire; oxidiser | Oxidizing gas category1
H271 | May cause fire or explosion; strong oxidiser | Oxidizing liquid category 1
H272 | May intensify fire; oxidiser | Oxidizing liquid category 2 Oxidizing liquid category 3
H280 | Contains gas under pressure; may explode if heated | Gases under pressure, compressed gas Gases under pressure, liquefied gas Gases under pressure, dissolved gas
H281 | Contains refrigerated gas; may cause cryogenic burns or injury | Gases under pressure, refrigerated liquefied gas
H290 | May be corrosive to metals Corrosive to metal | Corrosive to metal category 1
H300 | Fatal if swallowed | Acute toxicity category 1 (oral) Acute toxicity category 2 (oral)
H301 | Toxic if swallowed | Acute toxicity category 3 (oral)
H302 | Harmful if swallowed | Acute toxicity category 4 (oral)
H303 | Can be harmful if swallowed | Acute toxicity category 5 (oral)
H304 | May be fatal if swallowed and enters airways | Aspiration hazard category 1
H305 | May be harmful if swallowed and enters airways | Aspiration hazard category 2
H310 | Fatal in contact with skin | Acute toxicity category 1 (dermal) Acute toxicity category 2 (dermal)
H311 | Toxic in contact with skin | Acute toxicity category 3 (dermal)
H312 | Harmful in contact with skin | Acute toxicity category 4 (dermal)
H313 | May be harmful in contact with skin | Skin corrosion/irritation category 1(1A/1B/1C)
H315 | Causes skin irritation | Skin corrosion/irritation category 2
H316 | Causes light skin irritation | Skin corrosion/irritation category 3
H317 | May cause an allergic skin reaction | Skin sensitization category 1
H318 | Causes serious eye damage | Serious eye damage/eye irritation category 1
H319 | Causes serious eye irritation | Serious eye damage/eye irritation category 2A
H320 | Causes eye irritation | Serious eye damage/eye irritation category 2B
H330 | Fatal if inhaled | Acute toxicity category 1 (inhalation) Acute toxicity category 2 (inhalation)
H331 | Toxic if inhaled | Acute toxicity category 3 (inhalation)
H332 | Harmful if inhaled | Acute toxicity category 4 (inhalation)
H333 | Can be harmful if inhaled | Acute toxicity category 5 (inhalation)
H334 | May cause allergy or asthma symptoms or breathing difficulties if inhaled | Respiratory sensitization category 1
H335 | May cause respiratory irritation | Specific target organ toxicity-single exposure category 3
H336 | May cause drowsiness or dizziness | Specific target organ toxicity-single exposure category 3
H340 | May cause genetic defects (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Germ cell mutagenicity category 1(1A/1B)
H341 | Suspected of causing genetic defects (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Germ cell mutagenicity category 2
H350 | May cause cancer (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Carcinogenicity category 1 (1A/1B)
H351 | Suspected of causing cancer (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Carcinogenicity category 2
H360 | May damage fertility or the unborn child (state specific effect if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Reproductive toxicity category 1 (1A/1B)
H361 | Suspected of damaging fertility or the unborn child (state specific effect if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Reproductive toxicity category 2
H362 | May cause harm to breast-fed children | Effect on or via lactation
H370 | Causes damage to organs (or state all organs effected if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Specific target organ toxicity-single exposure category 1
H371 | May cause damage to organs (or state all organs effected if known) (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard) | Specific target organ toxicity-single exposure category 2
H372 | Causes damage to organs through prolonged or repeated exposure | Specific target organ toxicity- repeated exposure category 1
H373 | May cause damage to organs prolonged or repeated exposure | Specific target organ toxicity- repeated exposure category 2
H400 | Very toxic to aquatic life | Hazardous to the aquatic environment – acute toxicity category 1
H401 | Toxic to aquatic life | Hazardous to the aquatic environment – acute toxicity category 2
H402 | Harmful to aquatic life | Hazardous to the aquatic environment – acute toxicity category 3
H410 | Very toxic to aquatic life with long lasting effects | Hazardous to the aquatic environment – chronic toxicity category 1
H411 | Toxic to aquatic life with long lasting effects | Hazardous to the aquatic environment – chronic toxicity category 2
H412 | Harmful to aquatic life with long lasting effects | Hazardous to the aquatic environment – chronic toxicity category 3
H413 | May cause long lasting harmful effects to aquatic life | Hazardous to the aquatic environment – chronic toxicity category 4
GHS HAZARD STATEMENTS INFORMATION

## Slide 2
GHS PRECAUTIONARY STATEMENTS INFORMATION
Code (1) | General precautionary Statements-Prevention (2) | Hazard class (3) | Hazard category (4) | Conditions for use (5)
P201 | Obtain special instructions before use. | Explosives | Unstable explosive | 
 |  | Germ cell mutagenicity | 1A, 1B, 2 | 
 |  | Carcinogenicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | Effects on or via lactation | 
P202 | Do not handle until all safety precautions have been read and understood. | Explosives | Unstable explosive | 
 |  | Germ cell mutagenicity | 1A, 1B, 2 | 
 |  | Carcinogenicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | 1A, 1B, 2 | 
P210 | Keep away from heat/sparks/open flames/hot surfaces. — No smoking. | 1. Explosives | Divisions 1.1, 1.2, 1.3,1.4, 1.5 | Manufacturer/supplier to specify applicable ignition source(s).
 |  | Flammable gases | 1, 2 | 
 |  | Flammable aerosols | 1, 2 | 
 |  | Flammable liquids | 1, 2, 3 | 
 |  | Flammable solids | 1, 2 | 
 |  | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Pyrophoric liquids | 1 | 
 |  | Pyrophoric solids | 1 | 
 |  | Organic peroxides | Types A, B, C, D, E, F | 
 |  | Oxidising liquids | 1, 2, 3 | Specify to keep away from heat.
 |  | Oxidising solids | 1, 2, 3 | 
P211 | Do not spray on an open flame or other ignition source. | Flammable aerosols | 1, 2 | 
P220 | Keep/Store away from clothing/…/combustible materials. | Oxidising gases | 1 | …Manufacturer/supplier to specify incompatible materials.
 |  | Self-reactive chemicals | Types A, B, C,D, E, F | 
 |  | Oxidising liquids | 1 | …Manufacturer/supplier to specify incompatible materials. — specify to keep away from clothing as well as other incompatible materials.
 |  |  | 2, 3 | …Manufacturer/supplier to specify incompatible materials.
 |  | Oxidising solids | 1 | …Manufacturer/supplier to specify incompatible materials. — specify to keep away from clothing as well as other incompatible materials.
 |  |  | 2, 3 | …Manufacturer/supplier to specify incompatible materials.
 |  | Oxidising solids | Types A, B, C, D, E, F | 
P221 | Take any precaution to avoid mixing with combustibles/… | Oxidising liquids | 1, 2, 3 | …Manufacturer/supplier to specify incompatible materials.
 |  | Oxidising solids | 1, 2, 3 | 
P222 | Do not allow contact with air. | Pyrophoric liquids | 1 | 
 |  | Pyrophoric solids | 1 | 
P223 | Keep away from any possible contact with water, because of violent reaction and possible flash fire. | Chemicals which, in contact with water, emit flammable gases | 1, 2 | 
P230 | Keep wetted with … | Explosives | Divisions 1.1, 1.2, 1.3, 1.5 | …Manufacturer/supplier to specify appropriate material. — if drying out increases explosion hazard, except as needed for manufacturing or operating processes (e.g. nitrocellulose).
P231 | Handle under inert gas. | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
P232 | Protect from moisture. | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
P233 | Keep container tightly closed. | Flammable liquids | 1, 2, 3 | 
 |  | Acute toxicity (inhalation) | 1, 2, 3 | — if product is volatile so as to generate hazardous atmosphere.
 |  | Specific target organ toxicity — single exposure (respiratory tract Irritation) | 3 | 
 |  | Specific target organ toxicity — single exposure (narcosis) | 3 | 
P234 | Keep only in original container. | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Organic peroxides | Types A, B, C, D, E, F | 
 |  | Corrosive to metals | 1 | 
P235 | Keep cool. | Flammable liquids | 1, 2, 3 | 
 |  | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Self-heating chemicals | 1, 2 | 
 |  | Organic peroxides | Types A, B, C, D, E, F | 
P240 | Ground/bond container and receiving equipment. | Explosives | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | — if the explosive is electrostatically sensitive.
 |  | Flammable liquids | 1, 2, 3 | — if electrostatically sensitive material is for reloading. — if product is volatile so as to generate hazardous atmosphere.
 |  | Flammable solids | 1, 2 | — if electrostatically sensitive material is for reloading.
P241 | Use explosion-proof electrical/ventilating/lighting/ …/ equipment. | Flammable liquids | 1, 2, 3 | …Manufacturer/supplier to specify other equipment.
 |  | Flammable solids | 1, 2 | …Manufacturer/supplier to specify other equipment. — if dust clouds can occur.
P242 | Use only non-sparking tools. | Flammable liquids | 1, 2, 3 | 
P243 | Take precautionary measures against static discharge. | Flammable liquids | 1, 2, 3 | 
P244 | Keep reduction valves free from grease and oil. | Oxidising gases | 1 | 
P250 | Do not subject to grinding/shock/…/friction. | Explosives | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | …Manufacturer/supplier to specify applicable rough handling.
P251 | Pressurized container: Do not pierce or burn, even after use. | Flammable aerosols | 1, 2 | 
P260 | Do not breathe dust/fume/gas/mist/ vapours/spray. | Acute toxicity (inhalation) | 1, 2 | Manufacturer/supplier to specify applicable conditions.
 |  | Specific target organ toxicity — single exposure | 1, 2 | 
 |  | Specific target organ toxicity — repeated exposure | 1, 2 | 
 |  | Skin corrosion | 1A, 1B, 1C | — Specify do not breathe dusts or mists. — if inhalable particles of dusts or mists may occur during use.
 |  | Reproductive toxicity | Effects on or via lactation | 
P261 | Avoid breathing dust/fume/ gas/mist/vapours/spray. | Acute toxicity (inhalation) | 3, 4 | — Specify do not breathe dusts or mists. — if inhalable particles of dusts or mists may occur during use.
 |  | Respiratory sensitisation |  | 
 |  | Skin sensitisation |  | 
 |  | Specific target organ toxicity — single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity — single exposure; (narcosis) | 3 | 
P262 | Do not get in eyes, on skin, or on clothing | Acute toxicity (dermal) | 1, 2 | 
P263 | Avoid contact during pregnancy/ while nursing. | Reproductive toxicity | Effects on or via lactation | 
P264 | Wash … thoroughly after handling. | Acute toxicity (oral) | 1, 2, 3, 4 | Manufacturer/supplier to specify parts of the body to be washed after handling
 |  | Acute toxicity (dermal) | 1, 2 | 
 |  | Skin corrosion | 1A, 1B, 1C | 
 |  | Skin irritation | 2 | 
 |  | Eye irritation | 2 | 
 |  | Reproductive toxicity | Effects on or via lactation | 
 |  | Specific target organ toxicity — single exposure | 1, 2 | 
 |  | Specific target organ toxicity — repeated exposure | 1 | 
P270 | Do not eat, drink or smoke when using this product. | Acute toxicity (oral) | 1, 2, 3, 4 | 
 |  | Acute toxicity (dermal) | 1, 2 | 
 |  | Reproductive toxicity | Effects on or via lactation | 
 |  | Specific target organ toxicity — single exposure | 1, 2 | 
 |  | Specific target organ toxicity — repeated exposure | 1 | 
P271 | Use only outdoors or in a well-ventilated area. | Acute toxicity (inhalation) | 1, 2, 3, 4 | 
 |  | Specific target organ toxicity — single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity — single exposure; (narcosis) | 3 | 
P272 | Contaminated work clothing should not be allowed out of the workplace | Skin sensitisation | 1 | 
P273 | Avoid release to the environment. | Hazardous to the aquatic environment — acute aquatic hazard | — if this is not the intended use. | 
 |  | Hazardous to the aquatic environment — chronic aquatic hazard | 1, 2, 3, 4 | 
 |  | Hazardous to the ozone layer | 1 | 
P280 | Wear protective gloves/protective clothing/eye protection/face protection. | Explosives | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | Manufacturer/supplier to specify type of equipment. — Specify face protection.
 |  | Flammable liquids | 1, 2, 3 | Manufacturer/supplier to specify type of equipment. — Specify protective gloves and eye/face protection.
 |  | Flammable solids | 1, 2 | 
 |  | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Pyrophoric liquids | 1 | 
 |  | Pyrophoric solids | 1 | 
 |  | Self-reactive chemicals | 1, 2 | 
 |  | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
 |  | Oxidising liquids | 1, 2, 3 | 
 |  | Oxidising solids | 1, 2, 3 | 
 |  | Organic peroxides | Types A, B, C, D, E, F | 
 |  | Skin corrosion | 1A, 1B, 1C | Manufacturer/supplier to specify type of equipment. — Specify protective gloves/clothing and eye/face protection.
 |  | Skin irritation | 2 | Manufacturer/supplier to specify type of equipment. — Specify protective gloves.
 |  | Skin sensitisation | 1 | 
 |  | Serious eye damage/eye irritation | 1, 2 | Manufacturer/supplier to specify type of equipment. — Specify eye/face protection.
P281 | Use personal protective equipment as required. | Explosives | Unstable explosive | 
 |  | Germ cell mutagenicity | 1A, 1B, 2 | 
 |  | Carcinogenicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | 1A, 1B, 2 | 
P282 | Use personal protective equipment as required. | Gases under pressure | Refrigerated liquefied gas | 
P283 | Wear fire/flame resistant/retardant clothing. | Oxidising liquids | 1 | 
 |  | Oxidising solids | 1 | 
P284 | Wear respiratory protection. | Acute toxicity (inhalation) | 1, 2 | Manufacturer/supplier to specify equipment.
P285 | In case of inadequate ventilation wear respiratory protection. | Respiratory sensitisation | 1 | Manufacturer/supplier to specify equipment.
P231 + P232 | Handle under inert gas. Protect from moisture. | Chemicals which in contact with water, emit flammable gases | 1, 2, 3 | 
P235 + P410 | Keep cool. Protect from sunlight. | Self-heating chemicals | 1, 2 | 

## Slide 3
Code | General precautionary statements-Prevention | Hazard class | Hazard category | Conditions for use
P301 | IF SWALLOWED: | Acute toxicity (oral) | 1, 2, 3, 4 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Aspiration Hazard | 1 | 
P302 | IF ON SKIN: | Pyrophoric liquids | 1 | 
 |  | Acute toxicity (dermal) | 1, 2, 3, 4 | 
 |  | Skin corrosion/irritation | 2 | 
 |  | Skin sensitisation | 1 | 
P303 | IF ON SKIN (or hair): | Flammable liquids | 1, 2, 3 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
P304 | IF INHALED: | Acute toxicity (inhalation) | 1, 2, 3, 4 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Respiratory sensitisation | 1 | 
 |  | Specific target organ toxicity — single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity — single exposure; (narcosis) | 3 | 
P305 | IF IN EYES: | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Serious eye damage/ eye irritation | 1, 2 | 
P306 | IF ON CLOTHING: | Oxidising liquids | 1 | 
 |  | Oxidising solids | 1 | 
P307 | IF exposed: | Specific target organ toxicity — single exposure | 1 | 
P308 | IF exposed or concerned: | Germ cell mutagenicity | 1A, 1B, 2 | 
 |  | Carcinogenicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | Effects on or via lactation | 
P309 | IF exposed or if you feel unwell: | Specific target organ toxicity — single exposure | 2 | 
P310 | Immediately call a POISON CENTER or doctor/physician. | Acute toxicity (oral) | 1, 2, 3 | 
 |  | Acute toxicity (dermal) | 1, 2 | 
 |  | Acute toxicity (inhalation) | 1, 2 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Serious eye damage/eye irritation | 1 | 
 |  | Aspiration hazard | 1 | 
P311 | Call a POISON CENTER or doctor/physician. | Acute toxicity (inhalation) | 3 | 
 |  | Respiratory sensitisation | 1 | 
 |  | Specific target organ toxicity — single exposure | 1, 2 | 
P312 | Call a POISON CENTER or doctor/physician if you feel unwell. | Acute toxicity (oral) | 4 | 
 |  | Acute toxicity (dermal) | 3, 4 | 
 |  | Acute toxicity (inhalation) | 4 | 
 |  | Specific target organ toxicity — single exposure; (respiratory tract Irritation) | 3 | 
 |  | Specific target organ toxicity — single exposure; (narcosis) | 3 | 
P313 | Get medical advice/attention. | Skin corrosion/irritation | 2, 3 | 
 |  | Serious eye damage/eye irritation | 2 | 
 |  | Skin sensitisation | 1 | 
 |  | Germ cell mutagenicity | 1A, 1B, 2 | 
 |  | Carcinogenicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | Effects on or via lactation | 
P314 | Get medical advice/attention if you feel unwell. | Specific target organ toxicity — repeated exposure | 1, 2 | 
P315 | Get immediate medical advice/attention. | Gases under pressure | Refrigerated liquefied gas | 
P320 | Specific treatment is urgent (see … on this label). | Acute toxicity (inhalation) | 1, 2 | ….Reference to supplemental first aid instruction. — if immediate administration of antidote is required
P321 | Specific treatment (see … on this label). | Acute toxicity (oral) | 1, 2, 3 | ….Reference to supplemental first aid instruction. — if immediate administration of antidote is required
 |  | Acute toxicity (inhalation) | 3 | … Reference to supplemental first aid instruction. — if immediate specific measures are required.
 |  | Specific target organ toxicity — single exposure | 1 | … Reference to supplemental first aid instruction. — if immediate measures are required.
 |  | Skin sensitisation | 1 | … Reference to supplemental first aid instruction. — manufacturer/supplier may specify a cleansing agent if appropriate.
 |  | Skin corrosion/irritation | 1A, 1B, 1C, 2 | 
P322 | Specific measures (see …on this label). | Acute toxicity (dermal) | 1, 2, 3, 4 | … Reference to supplemental first aid instruction. — if immediate measures such as specific cleansing agent is advised.
P330 | Rinse mouth. | Acute toxicity (oral) | 1, 2, 3, 4 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
P331 | Do NOT induce vomiting. | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Aspiration hazard | 1 | 
P332 | If skin irritation occurs: | Skin corrosion/irritation | 2 | 
P333 | If skin irritation or rash occurs: | Skin sensitisation | 1 | 
P334 | Immerse in cool water/wrap in wet bandages. | Pyrophoric liquids | 1 | 
 |  | Pyrophoric solids | 1 | 
 |  | Chemicals which, in contact with water, emit flammable gases | 1, 2 | 
P335 | Brush off loose particles from skin. | Pyrophoric solids | 1 | 
 |  | Chemicals which, in contact with water, emit flammable gases | 1, 2 | 
P336 | Thaw frosted parts with lukewarm water. Do not rub affected area. | Gases under pressure | Refrigerated liquefied gas | 
P337 | If eye irritation persists: | Serious eye damage/eye irritation | 2 | 
P338 | Remove contact lenses, if present and easy to do. Continue rinsing. | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Serious eye damage/ eye irritation | 1, 2 | 
P340 | Remove victim to fresh air and keep at rest in a position comfortable for breathing. | Acute toxicity (inhalation) | 1, 2, 3, 4 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Specific target organ toxicity — single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity — single exposure; (narcosis) | 3 | 
P341 | If breathing is difficult, remove victim to fresh air and keep at rest in a position comfortable for breathing. | Respiratory sensitisation | 1 | 
P342 | If experiencing respiratory symptoms: | Respiratory sensitisation | 1 | 
P350 | Gently wash with plenty of soap and water. | Acute toxicity (dermal) | 1, 2 | 
P351 | Rinse cautiously with water for several minutes. | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Serious eye damage/eye irritation | 1, 2 | 
P352 | Wash with plenty of soap and water. | Acute toxicity (dermal) | 3, 4 | 
 |  | Skin corrosion/irritation | 2 | 
 |  | Skin sensitisation | 1 | 
P353 | Rinse skin with water/shower. | Flammable liquids | 1, 2, 3 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
P360 | Rinse immediately contaminated clothing and skin with plenty of water before removing clothes. | Oxidising liquids | 1 | 
 |  | Oxidising solids | 1 | 
P361 | Remove/Take off immediately all contaminated clothing. | Flammable liquids | 1, 2, 3 | 
 |  | Acute toxicity (dermal) | 1, 2, 3 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
P362 | Take off contaminated clothing and wash before reuse. | Skin corrosion/irritation | 2 | 
P363 | Wash contaminated clothing before reuse. | Acute toxicity (dermal) | 1, 2, 3, 4 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Skin sensitisation | 1 | 
P370 | In case of fire: | Explosives | Divisions 1.1, 1.2, 1.3, 1.4,1.5 | 
 |  | Oxidising gases | 1 | 
 |  | Flammable liquids | 1, 2, 3 | 
 |  | Flammable solids | 1, 2 | 
 |  | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Pyrophoric liquids | 1 | 
 |  | Pyrophoric solids | 1 | 
 |  | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
 |  | Oxidising liquids | 1, 2, 3 | 
 |  | Oxidising solids | 1, 2, 3 | 
P371 | In case of major fire and large quantities: | Oxidising liquids | 1 | 
 |  | Oxidising solids | 1 | 
P372 | Explosion risk in case of fire. | Explosives | Unstable explosives and Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | — except if explosives are 1.4S AMMUNITION AND COMPONENTS THEREOF
P373 | DO NOT fight fire when fire reaches explosives. | Explosives | Unstable explosives and Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | 
P374 | Fight fire with normal precautions from a reasonable distance. | Explosives | Division 1.4 | — if explosives are 1.4S AMMUNITION AND COMPONENTS THEREOF
P375 | Fight fire remotely due to the risk of explosion. | Self-reactive chemicals | Types A, B | 
 |  | Oxidising liquids | 1 | 
 |  | Oxidising solids | 1 | 
P376 | Stop leak if safe to do so. | Oxidising gases | 1 | 
P377 | Leaking gas fire: Do not extinguish, unless leak can be stopped safely. | Flammable gases | 1, 2 | 
P378 | Use … for extinction. | Flammable liquids | 1, 2, 3 | … Manufacturer/supplier to specify appropriate media — if water increases risk.
 |  | Flammable solids | 1, 2 | 
 |  | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Pyrophoric liquids | 1 | 
 |  | Pyrophoric solids | 1 | 
 |  | chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
 |  | Oxidising liquids | 1, 2, 3 | 
 |  | Oxidising solids | 1, 2, 3 | 
P380 | Evacuate area. | Explosives | Unstable explosives | 
 |  | Explosives | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | 
 |  | Self-reactive chemicals | Types A, B | 
 |  | Oxidising liquids | 1 | 
 |  | Oxidising solids | 1 | 
P381 | Eliminate all ignition sources if safe to do so. | Flammable gases | 1, 2 | 
P390 | Absorb spillage to prevent material damage. | Corrosive to metals | 1 | 
P391 | Collect spillage. | Hazardous to the aquatic environment – acute hazard | 1 | 
 |  | Hazardous to the aquatic environment – chronic hazard | 1, 2 | 

## Slide 4
Code | General precautionary statements - Response | Hazard class | Hazard category | Conditions for use
P301 + P310 | IF SWALLOWED: Immediately call a POISON CENTER or doctor/physician. | Acute toxicity (oral) | 1, 2, 3 | 
 |  | Aspiration hazard | 1 | 
P301 + P312 | IF SWALLOWED: Call a POISON CENTER or doctor/ physician if you feel unwell. | Acute toxicity (oral) | 4 | 
P301 + P330 + P331 | IF SWALLOWED: Rinse mouth. Do NOT induce vomiting. | Skin corrosion/irritation | 1A, 1B, 1C | 
P302 + P334 | IF ON SKIN: Immerse in cool water/wrap in wet bandages. | Pyrophoric liquids | 1 | 
P302 + P350 | IF ON SKIN: Gently wash with plenty of soap and water. | Acute toxicity (dermal) | 1, 2 | 
P302 + P352 | IF ON SKIN: Wash with plenty of soap and water. | Acute toxicity (dermal) | 3, 4 | 
 |  | Skin corrosion/irritation | 2 | 
 |  | Skin sensitisation | 1 | 
P303 + P361 + P353 | IF ON SKIN (or hair): Remove/Take off immediately all contaminated clothing. Rinse skin with water/shower. | Flammable liquids | 1, 2, 3 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
P304 + P340 | IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing. | Acute toxicity (inhalation) | 1, 2, 3, 4 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Specific target organ toxicity — single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity — single exposure; (narcosis) | 3 | 
P304 + P341 | IF INHALED: If breathing is difficult, remove victim to fresh air and keep at rest in a position comfortable for breathing. | Respiratory sensitisation | 1 | 
P305 + P351 + P338 | IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Serious eye damage/eye irritation | 1, 2 | 
P306 + P360 | IF ON CLOTHING: Rinse immediately contaminated clothing and skin with plenty of water before removing clothes. | Oxidising liquids | 1 | 
 |  | Oxidising solids | 1 | 
P307 + P311 | IF exposed: Call a POISON CENTER or doctor/physician. | Specific target organ toxicity — single exposure | 1 | 
P308 + P313 | IF exposed or concerned: Get medical advice/attention. | Germ cell mutagenicity | 1A, 1B, 2 | 
 |  | Carcinogenicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | Effects on or via lactation | 
P309 + P311 | IF exposed or if you feel unwell: Call a POISON CENTER or doctor/physician. | Specific target organ toxicity — single exposure | 2 | 
P332 + P313 | If skin irritation occurs: Get medical advice/attention. | Skin corrosion/irritation | 2 | 
P333 + P313 | If skin irritation or rash occurs: Get medical advice/ attention. | Skin sensitisation | 1 | 
P335 + P334 | Brush off loose particles from skin. Immerse in cool water/wrap in wet bandages. | Pyrophoric solids | 1 | 
 |  | Chemicals which, in contact with water, emit flammable gases | 1, 2 | 
P337 + P313 | If eye irritation persists: Get medical advice/attention. | Serious eye damage/ eye irritation | 2 | 
P342 + P311 | If experiencing respiratory symptoms: Call a POISON CENTER or doctor/physician. | Respiratory sensitisation | 1 | 
P370 + P376 | In case of fire: Stop leak if safe to do so. | Oxidizing gases | 1 | 
P370 + P378 | In case of fire: Use … for extinction. | Flammable liquids | 1, 2, 3 | 
 |  | Flammable solids | 1, 2 | 
 |  | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Pyrophoric liquids | 1 | 
 |  | Pyrophoric solids | 1 | 
 |  | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
 |  | Oxidising liquids | 1, 2, 3 | 
 |  | Oxidising solids | 1, 2, 3 | 
P370 + P380 | In case of fire: Evacuate area. | Explosives | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 | 
P370 + P380 + P375 | In case of fire: Evacuate area. Fight fire remotely due to the risk of explosion. | Self-reactive chemicals | Types A, B | 
P371 + P380 + P375 | In case of major fire and large quantities: Evacuate area. Fight fire remotely due to the risk of explosion. | Oxidising liquids | 1 | 
 |  | Oxidising solids | 1 | 

## Slide 5
Code | General precautionary statements - Storage | Hazard class | Hazard category | Conditions for use
P401 | Store … | Explosives | Unstable explosives and Divisions 1.1,1.2, 1.3, 1.4,1.5 | … in accordance with local/regional/national/ international regulations (to be specified).
P402 | Store in a dry place. | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
P403 | Store in a well-ventilated place. | Flammable gases | 1, 2 | — if product is volatile so as to generate hazardous atmosphere.
 |  | Oxidising gases | 1 | 
 |  | Gases under pressure | Compressed gas | 
 |  |  | Liquefied gas | 
 |  |  | Refrigerated Liquefied gas | 
 |  |  | Dissolved gas | 
 |  | Flammable liquids | 1, 2, 3 | 
 |  | Self-reactive chemicals | Types A, B, C,D, E, F | 
 |  | Acute toxicity (inhalation) | 1, 2, 3 | 
 |  | Specific target organ toxicity —single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity —single exposure; (narcosis) | 3 | 
P404 | Store in a closed container. | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
P405 | Store locked up. | Acute toxicity (oral) | 1, 2, 3 | 
 |  | Acute toxicity (dermal) | 1, 2, 3 | 
 |  | Acute toxicity (inhalation) | 1, 2, 3 | 
 |  | Skin corrosion/skin irritation | 1A, 1B, 1C | 
 |  | Germ cell mutagenicity | 1A, 1B, 2 | 
 |  | Carcinogenicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | 1A, 1B, 2 | 
 |  | Specific target organ toxicity — single exposure | 1, 2 | 
 |  | Specific target organ toxicity —single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity —single exposure; (narcosis) | 3 | 
 |  | Aspiration hazard | 1 | 
P406 | Store in corrosive resistant/ … container with a resistant inner liner. | Corrosive to metals | 1 | … Manufacturer/supplier to specify other compatible materials.
P407 | Maintain air gap between stacks/pallets. | Self-heating chemicals | 1, 2 | 
P410 | Protect from sunlight. | Flammable aerosols | 1, 2 | 
 |  | Gases under pressure | Compressed gas Liquefied gas Dissolved gas | 
 |  | Self-heating chemicals | 1, 2 | 
 |  | Organic peroxides | Types A, B, C, D, E, F | 
P411 | Store at temperatures not exceeding … oC/…oF. | Self-reactive chemicals | Types A, B, C, D, E, F | … Manufacturer/supplier to specify temperature
 |  | Organic peroxides | Types A, B, C, D, E, F | 
P412 | Do not expose to temperatures exceeding 50 oC/122 oF. | Flammable aerosols | 1, 2 | 
P413 | Store bulk masses greater than … kg/…lbs at temperatures not exceeding… oC/…oF. | Self-heating chemicals | 1, 2 | … Manufacturer/supplier to specify mass and temperature.
P420 | Store away from other materials. | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Self-heating chemicals | 1, 2 | 
 |  | Organic peroxides | Types A, B, C, D, E, F | 
P422 | Store contents under… | Pyrophoric liquids | 1 | … Manufacturer/supplier to specify appropriate liquid or inert gas
 |  | Pyrophoric solids | 1 | 
P402 + P404 | Store in a dry place. Store in a closed container. | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
P403 + P233 | Store in a well-ventilated place. Keep container tightly closed. | Acute toxicity (inhalation) | 1, 2, 3 | — if product is volatile so as to generate hazardous
 |  | Specific target organ hazardous toxicity atmosphere. — single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity — single exposure; (narcosis) | 3 | 
P403 + P235 | Store in a well-ventilated place. Keep cool. | Flammable liquids | 1, 2, 3 | 
 |  | Self-reactive chemicals | Types A, B, C, D, E, F | 
P410 + P403 | Protect from sunlight. Store in a well-ventilated place. | Gases under pressure | Compressed gas Liquefied gas Dissolved gas | 
P410 + P412 | Protect from sunlight. Do not expose to temperatures exceeding 50 oC/122oF. | Flammable aerosols | 1, 2 | 
P411 + P235 | Store at temperatures not exceeding … oC/…oF. Keep cool. | Organic peroxides | Types A, B, C, D, E, F | … Manufacturer/supplier to specify temperature.

## Slide 6
Code | General precautionary statements - Disposal | Hazard class | Hazard category | Conditions for use
P501 | Dispose of contents/container to … | Explosives | Unstable explosives and Divisions 1.1, 1.2, 1.3, 1.4,1.5 | … in accordance with local/regional/national/ international regulation (to be specified).
 |  | Flammable liquids | 1, 2, 3 | 
 |  | Self-reactive chemicals | Types A, B, C, D, E, F | 
 |  | Chemicals which, in contact with water, emit flammable gases | 1, 2, 3 | 
 |  | Oxidising liquids | 1, 2, 3 | 
 |  | Oxidising solids | 1, 2, 3 | 
 |  | Organic peroxides | Types A, B, C, D, E, F | 
 |  | Acute toxicity (oral) | 1, 2, 3, 4 | 
 |  | Acute toxicity (dermal) | 1, 2, 3, 4 | 
 |  | Acute toxicity (inhalation) | 1, 2 | 
 |  | Skin corrosion/irritation | 1A, 1B, 1C | 
 |  | Respiratory sensitisation | 1 | 
 |  | Skin sensitisation | 1 | 
 |  | Germ cell mutagenicity | 1A, 1B, 2 | 
 |  | Carcinogenicity | 1A, 1B, 2 | 
 |  | Reproductive toxicity | 1A, 1B, 2 | 
 |  | Specific target organ toxicity —single exposure | 1, 2 | 
 |  | Specific target organ toxicity —single exposure; (respiratory tract irritation) | 3 | 
 |  | Specific target organ toxicity —single exposure; (narcosis) | 3 | 
 |  | Specific target organ toxicity — repeated exposure | 1, 2 | 
 |  | Aspiration hazard | 1 | 
 |  | Hazardous to the aquatic environment — acute hazard | 1 | 
 |  | aquatic environment — acute hazard | 1, 2, 3, 4 | 
 |  | Hazardous to the ozone layer | 1 | 
P502 | Refer to manufacturer /supplier for information on recovery /recycling | Hazardous to the ozone layer | 1 | 

## Slide 7
Code | General precautionary Statements - Other | 
R20/21 | Harmful by inhalation and in contact with skin. | 
R38 | Irritating to skin. | 
S9 | Keep container in a well-ventilated place. | 
S16 | Keep away from sources of ignition | 
 | smoking. | 
S33 | Take precautionary measures against static | 
 | discharges | 
S36/37 | Wear suitable protective clothing and gloves. | 
S60 | This material and its container must be disposed of as hazardous waste. | 
F | Highly Flammable | 
Xn | Harmful | 
R11 | Highly flammable | 
R41 | Risk of serious damage to eyes | 
R48/20 | Harmful: danger of serious damage to health by prolonged exposure through inhalation. | 
R63 | Possible risk of harm to the unborn child. | 
R65 | Harmful: may cause lung damage if swallowed. | 
R67 | Vapours may cause drowsiness and dizziness. | 
S26 | In case of contact with eyes, rinse immediately with plenty of water and seek medical advice. | 
S36/37/39 | Wear suitable protective clothing, gloves and eye/face protection. | 
S62 | If swallowed, do not induce vomiting: seek medical advice immediately and show this container or label. | 
R34 | Causes burns. | 
European Union Physical properties |  | 
EUH001 | Explosive when dry | 
EUH006 | Explosive with or without contact with air | Unstable at ambient temperatures
EUH014 | Reacts violently with water | Reacts violently with water [e.g. acetyl chloride, alkali metals, titanium tetrachloride]
EUH018 | In use may form flammable/explosive vapour-air mixture | 
EUH019 | May form explosive peroxides | May form explosive peroxides [e.g. diethyl ether, 1,4-dioxane]
EUH044 | Risk of explosion if heated under confinement | Decompose explosively if heated in steel drum but not in less-strong containers
Health properties |  | 
EUH029 | Contact with water liberates toxic gas | Evolves acute tox cat 1-3 gases in contact with water or damp air [e.g. aluminium phosphide, phosphorous pentasulphide]
EUH031 | Contact with acids liberates toxic gas | Contact with acids liberates acute toxic cat 3 gas [e.g. sodium hypochlorite, barium polysulphide]
EUH032 | Contact with acids liberates very toxic gas | Contact with acids liberates acute toxic cat 1-2 gas [e.g. salts of hydrogen cyanide, sodium azide]
EUH066 | Repeated exposure may cause skin dryness or cracking | Repeated exposure may cause skin dryness or cracking, but not classified irritant
EUH070 | Toxic by eye contact | Toxicity during eye irritation test attributed to absorption through eye, not through mucous membranes
EUH071 | Corrosive to the respiratory tract | Inhalation tox test mortality due to corrosion OR classified corrosive to skin and likely to be inhaled
Environmental properties |  | 
EUH059 | Hazardous to the ozone layer | 
Other EU hazard statements |  | 
EUH201 | Contains lead. Should not be used on surfaces liable to be chewed or sucked by children. | 
EUH201A | Warning! Contains lead. | 
EUH202 | Cyanoacrylate. Danger. Bonds skin and eyes in seconds. Keep out of the reach of children. | 
EUH203 | Contains chromium(VI). May produce an allergic reaction. | 
EUH204 | Contains isocyanates. May produce an allergic reaction. | 
EUH206 | Warning! Do not use together with other products. May release dangerous gases (chlorine). | 
EUH207 | Warning! Contains cadmium. Dangerous fumes are formed during use. See information supplied by the manufacturer. Comply with the safety instructions. | 
EUH208 | Contains < name of sensitising substance>. May produce an allergic reaction. | 
EUH209 | Can become highly flammable in use. | 
EUH209A | Can become flammable in use. | 
EUH210 | Safety data sheet available on request. | 
EUH401 | To avoid risks to human health and the environment, comply with the instructions for use. | Product use is plant protection product (subject to 91/414/EEC)